## Slide 1: Predictive Maintenance of Gearbox
Uniconverge Technologies Pvt. Ltd.
By Samarth Ghare

## Slide 2: Background
Gearboxes are critical in manufacturing. Failure leads to downtime.
Vibration data can help detect faults early.
Dataset from SpectraQuest Gearbox Fault Simulator.

## Slide 3: Problem Statement
Detect whether a gearbox is healthy or has a broken tooth using vibration data from 4 sensors.

## Slide 4: Design & Data
- 4 sensors
- Healthy vs Broken under variable loads
- .txt files containing vibration readings

## Slide 5: Feature Engineering
Extracted per-sensor features:
- Mean, Std, RMS, Max, Min, Skewness, Kurtosis
- 28 features per sample (7 x 4 sensors)

## Slide 6: Model & Implementation
- RandomForestClassifier
- Train-Test Split (80/20)
- Model trained on feature data

## Slide 7: Results
- Accuracy: 100%
- Perfect classification for both classes
- Visualized using Confusion Matrix

## Slide 8: Learnings
- Time-series signal handling
- Feature extraction techniques
- Practical experience in predictive maintenance

## Slide 9: Future Work
- Add FFT-based features
- Try deep learning models (CNNs, LSTMs)
- Deploy to real-time systems or edge devices

## Slide 10: Contact
Prepared by: Samarth Ghare
Guided by: Uniconverge Technologies Pvt. Ltd.
GitHub: https://github.com/Samarth-Ghare